## Slide 1: Isotope Labeled Internal Standards in Skyline
Tutorial Webinar #12
With
Christina Ludwig (Proteomics Researcher)
Ariel Bensimon (Proteomics Researcher)

## Slide 2: Agenda
Welcome from the Skyline team!
Isotope Labeled Standards in Skyline
Quick intro with Brendan MacLean
with Ariel Bensimon
with Tina Ludwig
Audience Q&A – submit questions to Google Form:
https://skyline.gs.washington.edu/labkey/qa4skyline.url

## Slide 3: Lecture: Isotope Labeled Standards in Skyline Webinar , 1 December 2015 Christina Ludwig Ariel Bensimon TU Munich ETH Zürich Germany Switzerland

## Slide 4
Motivation – why use isotope labeled standards ?
For the correct identification of a peptide: selecting the correct peak

## Slide 5
Motivation – why use isotope labeled standards ?
For the accurate quantification of a peptide: accounting for sources of variation
We assume that extra sample handling does not introduce extra variation
cells or tissue
protein
peptides
MS data
data analysis
Protein extraction
Digestion & C18
Separation &acquisition
Signal processing
control
treated
Biological variation
Technical variation: sample prep
LC-MS variation
Post-MS analysis variation
Bantscheff, M., Lemeer, S., Savitski, M. M. & Kuster, B., Anal Bioanal Chem 404, 939–965 (2012).

## Slide 6
Outline
Introduction - Ariel
Improve confident peptide identification - Ariel
Improve quantitative precision and accuracy - Tina
How to get stable-isotope labeled information into a Skyline ?
Generating a reference for identification
Using a reference for peak selection
Using a reference for optimal quantification
Label-free versus label-based quantification
Metabolic, chemical, enzymatic and spike-in labeling
Relative versus absolute quantification
Single and multiple point calibration

## Slide 7
Stable-isotope labeling
Heavy reference standards are generated such that they carry one or several isotope-labeled atoms.
  typically used isotope-labeled atoms: 13C, 15N, 18O
  most common amino acids: K, R but also A, L, I, F, P, V.
  use of 2H less favorable due to chromatographic elution differences
Be aware of the purity of isotope labeling.
These heavy references are chemically identical to the endogenous (light) targets and hence we assume they show the same behavior in terms of
  sample preparation biases
  Chromatography
  ionization
  fragmentation

## Slide 8
Modifications tab
Settings>>peptide senttings>>modifications (see also webinar 10)
  You edit a set of possible isotope modifications; select those relevant for each of the labels
  You can define and name labels ; select those relevant for your experiment. Some appear in default
  You can select which (if any) label is the internal standard
  You assume the standard is present;
  Reverse is possible

## Slide 9
Insert peptides
Full name
Mass in []
Correct: Mass in {}
Edit>>Insert>>peptides (see also webinar 10)
Insert a light peptide sequence
Insert a modified peptide sequence

## Slide 10
Select precursors & transitions

## Slide 11
Modify peptides
Make sure these are first set in Modifications tab

## Slide 12
Add label

## Slide 13
Export & Results
Isotope label information can be selected in any report exported:
Pivot based on the isotope label
In results grid:
Results tutorial : https://skyline.gs.washington.edu/labkey/_webdav/home/software/Skyline/@files/tutorials/CustomReports-1_2.pdf

## Slide 14
Outline
Introduction - Ariel
Improve confident peptide identification - Ariel
Improve quantitative precision and accuracy - Tina
Take home messages
(General Tips and Tricks when working with isotope-labeled peptides - Tina)
How to get stable-isotope labeled information into a Skyline ?
Generating a reference for identification
Using a reference for peak selection
Using a reference for optimal quantification
Label-free versus label-based quantification
Relative versus absolute quantification

## Slide 15
Motivation – why use isotope labeled standards ?
For the correct identification of a peptide: selecting the correct peak

## Slide 16
Criteria for reliable peak identification
3. Signal intensity
time (min)
intensity
1. Co-elution
time (min)
intensity
2. Peak shape
time (min)
intensity
4. Correlation peak
intensities to library spectrum
y6
y9
y7
y11
m/z
intensity
time (min)
intensity
5. Correlation retention time
(empirical)

## Slide 17
Generating a reference for identification
We can use a synthetic standard to generate :
  A reference spectrum for the spectral library (see also webinar 4, tutorials)
  A reference retention time value , for the RT library (see webinar 7, tutorials)
Shotgun data
PRM data
SRM data
MS/MS search
Reference spectrum
Library building
Data conversation
https://skyline.gs.washington.edu/labkey/announcements/home/support/thread.view?rowId=20003
To read how is dotp calculated in Skyline:
Reference for retention time

## Slide 18
Generating a reference for identification
We can use a synthetic standard to generate a reference:
  peptide or protein standard.
  heavy or light standard (chemically identical).
  Skyline transfers information, if you activate the heavy label in Modifications.
Shotgun data
PRM data
SRM data
To ensure a good dotp: Perform an identification experiment with the same MS setup (CE etc) , as in the targeted experiment.

## Slide 19
Generating a reference for identification
We can use a synthetic standard to generate a reference spectrum for the spectral library in SRM:
SRM triggered MS2 on QTRAP: if a product ion is monitored above a threshold, switch to Enhanced Product Ion (switch Q3 to LIT, acquire full fragment scan).
  For assay generation (using synthetic standards).
    http://targetedproteomics.ethz.ch/downloads.html (tutorials 2013)
  For validation (of any endogenous peptide peak).
Targeted MS2: SRM triggered MS2 as well as PRM. In both modes, one can view the peptide MS/MS events using Skyline.
MS/MS search
Reference spectrum
Library building
Data conversation
Picotti, P., et al. (2010). High-throughput generation of selected reaction-monitoring assays for proteins and proteomes. Nat Methods 7, 43–46.
SRM data ?
SRM triggered MS2

## Slide 20
For SRM trig-MS2 files: Enable the Full-scan Enable ID matching in the view
Note: for PRM the parameters are different (webinar 3)
Targeted MS2 in Skyline

## Slide 21
Targeted MS2 in Skyline
https://skyline.gs.washington.edu/labkey/tutorial_library_explorer.url
When working with with synthetic standards for assay generation : ensure the quality of your spectra

## Slide 22
Generating a reference for identification
We can use a synthetic standard to generate a reference for the chromatogram library: heavy or light standard; peptide or protein standard.
Notes:
  In SRM: you would need to measure all the desired transitions.
  You will still get a dotp from a chromatogram library.
  Ensure similarity in MS setup (CE etc).
PRM data
SRM data
Reference chromatogram
Library building
All b,y ions
Webinar 11; Tutorial (chromatogram libraries)
Dotp: 0.95
Dotp: 0.85
Same peptide with different CEs

## Slide 23
Criteria for reliable peak identification
3. Signal intensity
time (min)
intensity
1. Co-elution
time (min)
intensity
2. Peak shape
time (min)
intensity
6. Correlation with
heavy-labeled standard
light
heavy
light
heavy
time (min)
intensity
4. Correlation peak
intensities to library spectrum
y6
y9
y7
y11
m/z
intensity
time (min)
intensity
5. Correlation retention time
(empiric or predicted*)

## Slide 24
View individual precurosors
light
heavy

## Slide 25
View pairs
View:
Total sum, no transition info
Same boundries
These heavy references are chemically identical to the endogenous (light) :
Co-elution
Same peak boundries

## Slide 26
Split graph

## Slide 27
Dotp, rdotp with library
Dotp : 0.95
Dotp: 0.96
Rdotp: 1

## Slide 28
Dotp, rdotp without library
Dotp ?
Dotp ?
Rdotp: 1

## Slide 29
Using reference standards for peak selection
No clear peak, A low dotp
Which should we select ?

## Slide 30
Using reference standards for peak selection
0 hours
6 hours
48 hours

## Slide 31
Using reference standards for peak selection
We can confidently state about absence : the endogenous peptide is below detectability

## Slide 32
Using reference standards for peak selection

## Slide 33
Using reference standards for peak selection
  If the standard is set to heavy, it will be used in peak picking

## Slide 34
Using reference standards for peak selection
Modified peptides & localization: we can use synthetic standards to generate a reference for the identification and quantification of the correct modification site (an example with phosphorylation):
reference
TDALTS[Phos]SPGR
reference
TDALTSS[Phos]PGR
http://targetedproteomics.ethz.ch/videos.html

## Slide 35
Using reference standards for peak selection
reference
TDALTS[Phos]SPGR
reference
TDALTSS[Phos]PGR

## Slide 36
Using reference standards for peak selection
Modified peptides & localization: we can use synthetic standards to generate a reference for the identification and quantification of the correct modification site :
reference
TDALTS[Phos]SPGR
reference
TDALTSS[Phos]PGR

## Slide 37
Generating a reference for quantification
We can use a synthetic standard to generate a reference for the best quantitative assay :
PRM data
SRM data
Reference assay for maximal sensitivity
Library building
https://skyline.gs.washington.edu/labkey/wiki/home/software/Skyline/page.view?name=tutorial_optimize_ce
http://targetedproteomics.ethz.ch/downloads.html
for example collision energy optimization

## Slide 38
Using standards for peptide identification - summary
Generating a reference for identification
Using a reference for peak selection
Using a reference for optimal quantification
Reference spectrum in library
Reference for retention time
Reference chromatogram
In library
Reference chromatogram
Peak selection: RT, rdotp, transition selection
Reference for parameters (CE)
Peptide identification
In targeted proteomics
  Per se, does not require isotope label standards
  Can be stored in Skyline, Panorama
  Using isotope label standards

## Slide 39
Improve confident peptide identification
Generating a reference for identification
Using a reference for peak selection
Using a reference for optimal quantification
Label-free versus label-based quantification
Relative versus absolute quantification
Reference chromatogram
Peak selection: RT, rdotp, transition selection
Peptide identification
In targeted proteomics
  Using isotope label standards
Improve quantitative precision and accuracy
Tina: