## Slide 1: Lecture: Isotope Labeled Standards in Skyline Webinar , 1 December 2015 Christina Ludwig Ariel Bensimon TU Munich ETH Zürich Germany Switzerland

## Slide 2
Outline
Introduction - Ariel
Improve confident peptide identification - Ariel
Improve quantitative precision and accuracy - Tina
How to get stable-isotope labeled information into a Skyline ?
Generating a reference for identification
Using a reference for peak selection
Using a reference for optimal quantification
Label-free versus label-based quantification
Metabolic, chemical, enzymatic and spike-in labeling
Relative versus absolute quantification
Single and multiple point calibration
Motivation – why use isotope labeled standards ?
Outline

## Slide 3
Motivation – why use isotope labeled standards ?
For the accurate quantification of a peptide: accounting for sources of variation
cells or tissue
protein
peptides
MS data
data analysis
Protein extraction
Digestion & C18
Separation &acquisition
Signal processing
Bantscheff, M., Lemeer, S., Savitski, M. M. & Kuster, B., Anal Bioanal Chem 404, 939–965 (2012).
Motivation – why use isotope labeled standards ?
The earlier an isotope-labeled standard is added into the samples during sample preparation, the more precise and accurate the results!

## Slide 4
The multitude of quantitative MS-applications
SILAC
ICAT
mTRAQ
iTRAQ
ICPL
AQUA
PSAQ
QconCAT
Super-SILAC
ALF
pREST
APEX
NSAF
IBAQ
emPAI
PAI
TMT
18O-labeling
15N-labeling
Dimethyl-labeling
SpikeTides
Label-free

## Slide 5
SILAC
ICAT
mTRAQ
iTRAQ
ICPL
AQUA
PSAQ
QconCAT
Super-SILAC
ALF
pREST
APEX
NSAF
IBAQ
emPAI
PAI
TMT
18O-labeling
15N-labeling
Dimethyl-labeling
SpikeTides
Label-free
The multitude of quantitative MS-applications

## Slide 6
Label-free versus label-based quantification
label-free
label-based
SILAC
ICAT
mTRAQ
iTRAQ
ICPL
TMT
15N-labeling
Dimethyl-labeling
SpikeTides
AQUA
PSAQ
QconCAT
pREST
Super-SILAC
18O-labeling
IBAQ
ALF
APEX
emPAI
NSAF
Label-free

## Slide 7
Label-free versus label-based quantification
label-free
label-based
Cost- and work-effective (at least
in terms of sample preparation)
applicable to all identified/quantified
proteins – proteome-wide
no increase in sample complexity -
high sensitivity
Major advantages label-free:
Can account for preparative and
analytical variabilities
Improved quantitative precision and
accuracy compared to label-free quant.
Improved confidence in peak
identification
Major advantages label-based:

## Slide 8
Label-free versus label-based quantification
label-free
label-based
SILAC
ICAT
mTRAQ
iTRAQ
ICPL
TMT
15N-labeling
Dimethyl-labeling
SpikeTides
AQUA
PSAQ
QconCAT
pREST
Super-SILAC
18O-labeling
IBAQ
ALF
APEX
emPAI
NSAF
Label-free

## Slide 9
Stable-isotope labeling
Strategies for incorporating stable-isotopes
3. Enzymatic labeling
2. Chemical labeling
1. Metabolic labeling
4. Spike-in of isotope-labeled standards
label-based
SILAC
15N-labeling
For example:
TMT
iTRAQ
Dimethyl-labeling
For example:
synthetic peptides
protein standards
For example:
18O-labeling
For example:

## Slide 10
Stable-isotope labeling
Pros and Cons of stable-isotope labeling strategies
3. Enzymatic labeling
2. Chemical labeling
1. Metabolic labeling
4. Spike-in of isotope-labeled standards
label-based
Strengths
+ eliminates best preparative and analytical variabilities (combination of light and heavy very early, on cell level)
Weaknesses
- compatible with growing cells only
- significantly increased sample complexity
Strengths
+ Compatible with any protein source
+ Multiplexing possible
Weaknesses
- Potential for side reactions
- incomplete reactions
- Typically carried out on the peptide level
Strengths
+ Compatible with any protein source
+ protein digestion and labeling one step
Weaknesses
- variable incorporation of 18O atoms
- Small mass shifts of 2 to 4 Da
Strengths
+ Compatible with any sample type
+ Maximal confidence in correct peak identification
+ Minimal increase in sample complexity
Weaknesses
- expansive
- applicable to limited number of proteins

## Slide 11
Stable-isotope labeling
Strategies for incorporating stable-isotopes
3. Enzymatic labeling
2. Chemical labeling
1. Metabolic labeling
4. Spike-in of isotope-labeled standards
label-based
SILAC
15N-labeling
For example:
TMT
iTRAQ
Dimethyl-labeling
For example:
synthetic peptides
protein standards
For example:
18O-labeling
For example:

## Slide 12
Stable-isotope labeling
Strategies for incorporating stable-isotopes
3. Enzymatic labeling
2. Chemical labeling
1. Metabolic labeling
4. Spike-in of isotope-labeled standards
label-based
SILAC
15N-labeling
For example:
TMT
iTRAQ
Dimethyl-labeling
For example:
synthetic peptides
protein standards
For example:
18O-labeling
For example:

## Slide 13
Stable-isotope labeling
1. Metabolic labeling
Condition A
light (12C 14N)
arginine and lysine
Condition B
heavy (13C 15N)
arginine and lysine
Condition A
light 14N
Condition B
heavy 15N
(15N-labeled (NH4)2SO4)
m/z
Intensity
m/z
Intensity
SILAC
15N labeling
constant mass shift
8 Da (lysine) or 10 Da (arginine)
 variable mass shift depending on the number of N-atoms in the peptide/fragment
Skyline supports metabolic labeling

## Slide 14
Modifications tab
  You can select a set of possible isotope modifications; enable those relevant for the label.
  You can define and name labels ; select those relevant for your experiment.
  You can select which (if any) label is the internal standard
Skyline supports metabolic labeling
1. Metabolic labeling

## Slide 15
Stable-isotope labeling
Skyline supports metabolic labeling
1. Metabolic labeling
SILAC
15N labeling
 Peptide Settings  Modifications  Isotope Modification
1. Define isotope modifications

## Slide 16
Stable-isotope labeling
Skyline supports metabolic labeling
1. Metabolic labeling
SILAC
15N labeling
2. Create additional label type

## Slide 17
Stable-isotope labeling
Skyline supports metabolic labeling
1. Metabolic labeling
SILAC
15N labeling
3. Define Label Types

## Slide 18
Stable-isotope labeling
1. Metabolic labeling
SILAC
Skyline supports metabolic labeling
4. Isotope labeled variants will appear in peptide list
15N labeling
D 5 Da
D 10 Da
D 6.5 Da
D 12 Da
D 11 Da
D 8 Da

## Slide 19
Stable-isotope labeling
1. Metabolic labeling
Skyline supports metabolic labeling
Combination of several
isotope modification types in a single Skyline document is possible!!!!
light AND SILAC and 15N labeling

## Slide 20
Stable-isotope labeling
1. Metabolic labeling
Skyline supports metabolic labeling
Combination of several
isotope modification types in a single Skyline document is possible!!!!

## Slide 21
Stable-isotope labeling
Strategies for incorporating stable-isotopes
3. Enzymatic labeling
2. Chemical labeling
1. Metabolic labeling
4. Spike-in of isotope-labeled standards
label-based
SILAC
15N-labeling
For example:
TMT
iTRAQ
Dimethyl-labeling
For example:
synthetic peptides
protein standards
For example:
18O-labeling
For example:

## Slide 22
Stable-isotope labeling
Spike-in of isotope-labeled standards
synthetic peptides
NH2
COOH
13C- 15N-labeled C-terminal
amino acid (lysine/arginine)
Different purity forms available from various companies:
Crude peptides = cheap
 Library generation and relative quant.
Highly purified peptides (AQUA/SIS) = expansive
 Absolute quant.
concatenated
peptides
plasmid
cloning of concatenated
peptides (possibly from
different proteins) QconCAT
overexpression in
labeled medium
purification and concentration determination
co-digestion with endogenous proteins
full-length
recombinant proteins
plasmid
cloning of the complete protein
overexpression of the target protein in labeled medium
purification and concentration determination
co-digestion with endogenous protein
4. Spike-ins

## Slide 23
Skyline supports spike-in labeling
4. Spike-in
1. Define isotope modifications
Different to SILAC modification!!!
synthetic peptides
NH2
COOH
13C- 15N-labeled C-terminal
amino acid (lysine/arginine)
Different purity forms available from various companies:
Crude peptides = cheap
 Library generation and relative quant
Highly purified peptides (AQUA/SIS) = expansive
 Absolute quant.

## Slide 24
1. Define isotope modifications
2. Create additional label type
4. Spike-in
Skyline supports spike-in labeling
synthetic peptides
NH2
COOH
13C- 15N-labeled C-terminal
amino acid (lysine/arginine)
Different purity forms available from various companies:
Crude peptides = cheap
 Library generation and relative quant
Highly purified peptides (AQUA/SIS) = expansive
 Absolute quant.

## Slide 25
1. Define isotope modifications
2. Create additional label type
3. Define Label Types
4. Spike-in
Skyline supports spike-in labeling
synthetic peptides
NH2
COOH
13C- 15N-labeled C-terminal
amino acid (lysine/arginine)
Different purity forms available from various companies:
Crude peptides = cheap
 Library generation and relative quant
Highly purified peptides (AQUA/SIS) = expansive
 Absolute quant.

## Slide 26
1. Define isotope modifications
2. Create additional label type
4. Spike-in
3. Define Label Types
4. Isotope labeled variants will appear in peptide list
D 5 Da
D 5 Da
Skyline supports spike-in labeling
synthetic peptides
NH2
COOH
13C- 15N-labeled C-terminal
amino acid (lysine/arginine)
Different purity forms available from various companies:
Crude peptides = cheap
 Library generation and relative quant
Highly purified peptides (AQUA/SIS) = expansive
 Absolute quant.

## Slide 27
Stable-isotope labeling
Tutorial-6 “Manual SRM data analysis in Skyline” Zürich course
http://targetedproteomics.ethz.ch/tutorials2014/Tutorial-6_ManualAnalysis.pdf
http://targetedproteomics.ethz.ch/downloads.html
Mycobacterium tuberculosis (Mtb) total cell extracts
  Three different time points of hypoxia: 0h, 6h, and 48h
10 target proteins represented by 3 peptides each
 total of 30 peptides
30 isotopically labelled crude synthetic reference peptides available and spiked into each sample at the same concentration
Tryptic Digest
Protein Extraction
LC Retention Time
Intensity
SRM
heavy reference peptides
Task:
Analyze the data twice: Once label-free, once label-based!
Investigate the quantitative differences.

## Slide 28
Stable-isotope labeling
6h
0h
0h
6h
Tutorial-6 “Manual SRM data analysis in Skyline” Zürich course
http://targetedproteomics.ethz.ch/tutorials2014/Tutorial-6_ManualAnalysis.pdf

## Slide 29
Stable-isotope labeling
3. right mouse click on „Peak Areas“ window
“Peak Area” viewing options in Skyline
1. Settings  Document Settings
2. View  Results Grid

## Slide 30
Stable-isotope labeling
Is the detected fold-change of peptide AQAATAGIDDLRPALIR between condition 0h and 6h statistical significant?
right mouse click on „Peak Areas“ window
Coefficient of variation in %
“Peak Area” viewing options in Skyline

## Slide 31
Stable-isotope labeling
Simple group comparison within Skyline
Tutorial „Processing Grouped Study data“: https://skyline.gs.washington.edu/labkey/tutorial_grouped.url

## Slide 32
Stable-isotope labeling
Simple group comparison within Skyline
With a confidence of 99% (adj. p-value < 0.01) peptide AQAATAGIDDLRPALIR does
not change significant between 0h and 6h!
Confidence interval whiskers
Tutorial „Processing Grouped Study data“: https://skyline.gs.washington.edu/labkey/tutorial_grouped.url

## Slide 33
Stable-isotope labeling
6h
0h
6h
0h
0h
6h
Tutorial-6 “Manual SRM data analysis in Skyline”
http://targetedproteomics.ethz.ch/tutorials2014/Tutorial-6_ManualAnalysis.pdf

## Slide 34
Stable-isotope labeling
6h
0h
6h
0h
0h
6h
Tutorial-6 “Manual SRM data analysis in Skyline”
http://targetedproteomics.ethz.ch/tutorials2014/Tutorial-6_ManualAnalysis.pdf

## Slide 35
Stable-isotope labeling
6h
0h
6h
0h
0h
6h
Tutorial-6 “Manual SRM data analysis in Skyline”
http://targetedproteomics.ethz.ch/tutorials2014/Tutorial-6_ManualAnalysis.pdf

## Slide 36
Stable-isotope labeling
right mouse click on „Peak Areas“ window
“Peak Area” viewing options in Skyline

## Slide 37
Stable-isotope labeling
right mouse click on „Peak Areas“ window
“Peak Area” viewing options in Skyline

## Slide 38
Stable-isotope labeling
right mouse click on „Peak Areas“ window
Coefficient of variation in %
“Peak Area” viewing options in Skyline

## Slide 39
Stable-isotope labeling
Simple group comparison within Skyline
Tutorial „Processing Grouped Study data“: https://skyline.gs.washington.edu/labkey/tutorial_grouped.url

## Slide 40
Stable-isotope labeling
Simple group comparison within Skyline
Label-free
Label-based
Conclusion: Spike-in of isotope labeled peptides helps to account for sample preparation variabilites from the spike-in moment on
(no protein extraction or digestion variabilities!!!).
Thereby quantitative precision and accuracy get improved!

## Slide 41
The multitude of quantitative MS-applications
SILAC
ICAT
mTRAQ
iTRAQ
ICPL
AQUA
PSAQ
QconCAT
Super-SILAC
ALF
pREST
APEX
NSAF
IBAQ
emPAI
PAI
TMT
18O-labeling
15N-labeling
Dimethyl-labeling
SpikeTides
Label-free

## Slide 42
Relative versus absolute protein quantification
SILAC
ICAT
mTRAQ
iTRAQ
ICPL
AQUA
PSAQ
QconCAT
ALF
APEX
IBAQ
emPAI
TMT
18O-labeling
15N-labeling
Dimethyl-labeling
SpikeTides
relative
absolute
AQUA
PSAQ
QconCAT
ALF
pREST
APEX
emPAI
IBAQ
NSAF
Label-free

## Slide 43
Definition of absolute versus relative protein quantification
protein ratio
Relative quantification
healthy
disease
samples
output
1 : 2
2-fold upregulated
≥ 2 samples
relative comparison of the
same protein between samples
comparison of the same protein
between samples +
comparison of different proteins
within the same sample
Absolute quantification
protein
concentration
copies/cell
fmol/µg extract
ng/ml body fluid
≥ 1 samples

## Slide 44
MS-based absolute protein quantification strategies
absolute
label-free
absolute
label-based
gold-standard -
more precise !!!!

## Slide 45
absolute label-based quantification
quantification
value:
ratio to a reference with
known absolute concentration
Label-based absolute protein quantification

## Slide 46
Stable-isotope labeling
Strategies for incorporating stable-isotopes
3. Enzymatic labeling
2. Chemical labeling
1. Metabolic labeling
4. Spike-in of isotope-labeled standards
label-based

## Slide 47
absolute label-based quantification
quantification
value:
ratio to a reference with
known absolute concentration
plasmid
quantification
approach:
synthetic
peptides
labeled
proteins
concatenated
peptides
plasmid
AQUA
QconCAT
PSAQ
Label-based absolute protein quantification

## Slide 48
Absolute quantification – internal single point calibration
1.37
fold
68.5 fmol
reference peptide (heavy)
endogenous peptide (light)
Chart: MS signal intensity
| 0 | 800000
 | 0 | 50
50 fmol
Single point calibration
Assumptions of internal single point calibration:
Measurements are carried out within the linear dynamic range of the mass spectrometer
ratio light/heavy
= 1.37
spike-in concentration
50 fmol
Absolute quantification requires comparison to a reference molecule at a known concentration.
Linear correlation between MS signal intensity and absolute concentration with a
slope of 1 and an axis intercept of 0.

## Slide 49
Absolute quantification – multiple point calibration curve
Work with dilution series of isotope-labeled reference peptides/proteins
Advantages of multiple point calibration:
You can account for linear peptide responses which do NOT have slope = 1 and axis intercept = 0
Limitations of multiple point calibration:
Requires multiple injections (time and sample investment)
Best  Generate an external calibration curve once and use the obtained linear equation for absolute quantification
concentration, fmol/µl
intensity
linear equation:
y = 2.2E6x – 1.4E5

## Slide 50
Isotope-labeled absolute quantification supported within Skyline
https://skyline.gs.washington.edu/labkey/tutorial_absolute_quant.url
New implementations for internal single point and multiple point calibration curves
are already available in Skyline-daily and are coming soon in Skyline public….
Current Skyline Tutorial online available:

## Slide 51
Internal single-point absolute quantification supported within Skyline
Published data set:
Schubert O. T. & Ludwig C., et al. Cell host & microbe 18, 96-108, doi:10.1016/j.chom.2015.06.001 (2015).
Panorama link: https://panoramaweb.org/labkey/Mtb_anchors.url
Motivation of the data set:
Absolutely quantify 30 proteins in Mycobacterium Tuberculosis over 24 samples using
1-2 AQUA peptides per protein.
Points to consider regarding sample preparation:
Spike-in AQUA peptides into all samples.
Keep the concentration for a given AQUA peptide over all samples constant
Try to select a spike-in AQUA concentration close to 1:1 light : heavy
 If a peptide is strongly regulated over the samples of interest a 1:1 ratio is of course
not possible, try to select a spike-in concentration between highest and lowest sample

## Slide 52
Internal single-point absolute quantification supported within Skyline

## Slide 53
Peptide Settings  Quantification
View  Document Grid  Views  Peptide Quantification
Copy paste spike-in concentrations of each AQUA peptide in fmol/µg
Internal single-point absolute quantification supported within Skyline

## Slide 54
View  Document Grid  Views  Peptide Ratio Results
Internal single-point absolute quantification supported within Skyline

## Slide 55
Multiple-point absolute quantification supported within Skyline
View  Document Grid  Views  Replicates
Peptide Settings  Quantification

## Slide 56
Multiple-point absolute quantification supported within Skyline
View  Document Grid  Views  Peptide Quantification

## Slide 57
Take-home messages - Quantification
For every research project the optimal quantitative approach must be selected accordingly (label-free or label-based, relative or absolute)
 Skyline supports label-free as well as all 4 different subtypes of label-based quantification approaches (metabolic, enzymatic, chemical, spike-in)
 Skyline supports internal single-point as well as multiple point absolute quantification
Isotope-labeling helps to account for various types of variabilities (during sample preparation and LC-MS) and thereby to improve quantitative precision and accuracy!

## Slide 58
Acknowledgements
Targeted Proteomics Course Zürich – Team:
Prof. Ruedi Aebersold (ETH Zürich)
Brendan MacLean (University of Washington)
Prof. Mike MacCoss (University of Washington)
The whole Skyline Team
Prof. Olga Vitek (Northeastern University)
Prof. Bruno Domon (Luxembourg Institute of Health)
Olga Schubert (UCLA)
Ben Collins (ETH Zürich)
Betty Friedrich (ETH Zürich)
Ludovic Gillet (ETH Zürich)
Meena Choi (Purdue University)
Lukas Reiter (Biognosys)
Claudio Escher (Biognosys)
Oliver Rinner (Biognosys)
Eduard Sabido (CRG Barcelona)
Dario Amodei (Google)
Jarrett Egertson (University of Washington)
Ralph Schiess (ProteoMedix)
Paola Picotti (ETH Zürich)

## Slide 59: Learn More
Webinar #13: in January
Weeklong Course at IIT-Bombay
  December 10-14 - Full
Weeklong Courses 2016
  ETH, Zurich – February 8-12 - Full
  Buck Institute, San Francisco – March 7-11 – Register now!
  Northeastern University, Boston – May 2-6
  University of Washington, Seattle – July 18-22
  PRBB, Barcelona – November 13-18
Workshops 2016
  US HUPO, Boston – March 13

## Slide 60: Questions?
Ask any questions you have on modifications in Skyline at the following form: http://tinyurl.com/QA4Skyline
Take the post-webinar survey:
http://tinyurl.com/Survey4Webinar

## Slide 61: Tutorial Webinar #12
This ends this Skyline Tutorial Webinar.
Please give us feedback on the webinar at the following survey:
http://tinyurl.com/Survey4Webinar
A recording of today’s meeting will be available shortly at the Skyline website.
We look forward to seeing you at a future Skyline Tutorial Webinar.

## Slide 62
Additional slide material Christina Ludwig

## Slide 63
Isotope-labeled synthetic peptides can be “polluted” with the light form.
 Make sure what you are measuring in the light channel is not a “pollution” coming form the synthetic peptide (ratios close to 1:1 help!)
Tips and tricks: Isotope impurity!

## Slide 64
Isobaric transition interferences between heavy and light form of a peptide can make exclusions of such transitions necessary!
 Investigate your data!
Tips and tricks: Isobaric transition interferences
D 0.93 m/z
D . 0.06 m/z

## Slide 65
The isotopic pattern of the light and heavy peptide form is not perfectly equal!
 Hence, high resolution accurate mass data (PRM, DIA), where quantification gets based on the monoisotopic peak (as performed in Skyline!), must get corrected for the different theoretical isotopic pattern.
Tips and tricks: Different isotopic envelopes between light and heavy
1.1% 13C in
75 C-atoms
1.1% 13C in
69 (75-6) C-atoms
7% increase for 75 C-atom peptide
Standard peptide
(15 aa 75 C-atoms)
Figure adapted from Mike MacCoss
Mass Spectrometry Signal Calibration for Protein Quantitation, technical note, Cambridge Isotope Laboratories

## Slide 66
Significant Losses of AQUA peptides due to attachment to surfaces, degradation, freezing-thawing cycles, etc.
Issue when handling AQUA peptides (highly purified peptide solutions with precisely determined concentration):
Tips and tricks: Handling AQUA peptides
Tips:
 work with low-binding vessels and low-binding pipetting tips
 whenever possible use glass ware
 whenever possible use a complex sample background or a BSA solution as blocking reagent
 aliquote your standard stock solution upon arrival to avoid freezing-thawing cycles
 only purchase standards with known concentration in solution (not lyophilized to avoid any resuspension step)

## Slide 67
Stable-isotope labeling
Strategies for incorporating stable-isotopes
3. Enzymatic labeling
2. Chemical labeling
1. Metabolic labeling
4. Spike-in of isotope-labeled standards
18O-labeling
SILAC
15N-labeling
TMT
iTRAQ
Dimethyl-labeling
synthetic peptides
protein standards
label-based
For example:
For example:
For example:
For example:

## Slide 68
Skyline supports chemical labeling
Dimethyl labeling
reactivity for primary amines
(N-terminus and Lysine residues)
Boersema, P. J. et al., Nature Protocols, 4, 484-494 (2009).
2. Chemical labeling
+ 28 Da light
+ 36 Da heavy
+ 32 Da medium
+ 4 Da
+ 8 Da

## Slide 69
Modifications tab
  You can select a set of possible isotope modifications; enable those relevant for the label.
  You can define and name labels ; select those relevant for your experiment.
  You can select which (if any) label is the internal standard
Skyline supports chemical labeling
2. Chemical labeling
  Additionally needed

## Slide 70
Skyline supports chemical labeling
Dimethyl labeling
reactivity for primary amines
(N-terminus and Lysine residues)
Boersema, P. J. et al., Nature Protocols, 4, 484-494 (2009).
1. Define structural modification
2. Chemical labeling
+ 28 Da light
+ 36 Da heavy
+ 32 Da medium
+ 4 Da
+ 8 Da

## Slide 71
Skyline supports chemical labeling
Dimethyl labeling
reactivity for primary amines
(N-terminus and Lysine residues)
+ 28 Da light
Boersema, P. J. et al., Nature Protocols, 4, 484-494 (2009).
+ 36 Da heavy
+ 32 Da medium
2. Define isotope modification
2. Chemical labeling
+ 4 Da
+ 8 Da

## Slide 72
Skyline supports chemical labeling
Dimethyl labeling
reactivity for primary amines
(N-terminus and Lysine residues)
+ 28 Da light
Boersema, P. J. et al., Nature Protocols, 4, 484-494 (2009).
+ 36 Da heavy
+ 32 Da medium
2. Define isotope modification
2. Chemical labeling
+ 4 Da
+ 8 Da

## Slide 73
Skyline supports chemical labeling
Dimethyl labeling
reactivity for primary amines
(N-terminus and Lysine residues)
+ 28 Da light
Boersema, P. J. et al., Nature Protocols, 4, 484-494 (2009).
+ 36 Da heavy
+ 32 Da medium
2. Chemical labeling
3. Create additional label type
4. Define Label Types
+ 4 Da
+ 8 Da

## Slide 74
Skyline supports chemical labeling
Dimethyl labeling
reactivity for primary amines
(N-terminus and Lysine residues)
+ 28 Da light
Boersema, P. J. et al., Nature Protocols, 4, 484-494 (2009).
+ 36 Da heavy
+ 32 Da medium
5. Isotope labeled variants will appear in peptide list
2. Chemical labeling
D 2 Da
D 2 Da
D 4 Da
D 4 Da
+ 4 Da
+ 8 Da

## Slide 75
Skyline supports chemical labeling
iTRAQ/TMT
(isobaric tags for relative and absolute quantification / tandem mass tags)
 reactivity for primary amines
(N-terminus and Lysine residues)
Reporter
Balance
Reactive group
Amine specific
MReporter + MBalance = Constant
Mix all samples
for one
MS/MS analysis
30
29
28
31
115
116
117
114
2. Chemical labeling
1. Define structural modification

## Slide 76
Skyline supports chemical labeling
2. Chemical labeling
2. Define reporter ions
iTRAQ/TMT
(isobaric tags for relative and absolute quantification / tandem mass tags)
 reactivity for primary amines
(N-terminus and Lysine residues)
Reporter
Balance
Reactive group
Amine specific
MReporter + MBalance = Constant
Mix all samples
for one
MS/MS analysis
30
29
28
31
115
116
117
114

## Slide 77
Skyline supports chemical labeling
2. Chemical labeling
3. Labeled variants will appear in peptide list
iTRAQ/TMT
(isobaric tags for relative and absolute quantification / tandem mass tags)
 reactivity for primary amines
(N-terminus and Lysine residues)
Reporter
Balance
Reactive group
Amine specific
MReporter + MBalance = Constant
Mix all samples
for one
MS/MS analysis
30
29
28
31
115
116
117
114

## Slide 78
Stable-isotope labeling
Strategies for incorporating stable-isotopes
3. Enzymatic labeling
2. Chemical labeling
1. Metabolic labeling
4. Spike-in of isotope-labeled standards
18O-labeling
SILAC
15N-labeling
TMT
iTRAQ
Dimethyl-labeling
synthetic peptides
protein standards
label-based
For example:
For example:
For example:
For example:

## Slide 79
Skyline supports enzymatic labeling
+4 Da
Proteolytic 18O labeling
Miyagi, M. & Rao, K. C. S., Mass Spectrom Rev 26, 121–136 (2007).
3. Enzymatic labeling
Reaction 1 (peptide bond cleavage):
Reaction 2 (carboxyl oxygen exchange):
+2 Da
+4 Da

## Slide 80
Skyline supports enzymatic labeling
Proteolytic 18O labeling
1. Define isotope modifications
3. Enzymatic labeling
Reaction 1 (peptide bond cleavage):
Reaction 2 (carboxyl oxygen exchange):
+2 Da
+4 Da

## Slide 81
Skyline supports enzymatic labeling
Proteolytic 18O labeling
1. Define isotope modifications
2. Create additional label type
3. Enzymatic labeling
Reaction 1 (peptide bond cleavage):
Reaction 2 (carboxyl oxygen exchange):
+2 Da
+4 Da

## Slide 82
Skyline supports enzymatic labeling
Proteolytic 18O labeling
1. Define isotope modifications
2. Create additional label type
3. Define Label Types
3. Enzymatic labeling
Reaction 1 (peptide bond cleavage):
Reaction 2 (carboxyl oxygen exchange):
+2 Da
+4 Da

## Slide 83
Skyline supports enzymatic labeling
Proteolytic 18O labeling
1. Define isotope modifications
2. Create additional label type
3. Define Label Types
4. Isotope labeled variants will appear in peptide list
3. Enzymatic labeling
D 1 Da
D 1 Da
Reaction 1 (peptide bond cleavage):
Reaction 2 (carboxyl oxygen exchange):
+2 Da
+4 Da

## Slide 84
For which projects does absolute
protein quantification really matter?
absolute
protein
concentration
protein complex stoichiometries
mathematical
modeling
rate constants
kinetic fluxes
energy budget
etc.
3 : 2 : 1
data cross-comparison
inter-experimental
inter-laboratory
Inter-MS platform
inter-organism
protein biomarker development
quality control
therapeutic analysis
food safety
sports drug testing
etc.
pharmaceutical and biomedical industry

## Slide 85
Stable-isotope labeling
The time-point of heavy-light sample combination matters!
The more early an isotope-labeled standard is added into the samples during sample preparation, more accurate the results!
Metabolic
Chemical
Spike-in standards
label-free
cells or tissue
protein
peptides
MS data
data analysis
Bantscheff, M., Lemeer, S., Savitski, M. M. & Kuster, B., Anal Bioanal Chem 404, 939–965 (2012).