## Slide 1: “Research-grade” Targeted Proteomics Assay Development: PRMs for PTM Studies with Skyline or, “How I learned to ditch the triple quad and love the QE”
Jacob D. Jaffe
Skyline Webinar July 2015

## Slide 2: Outline
Definitions
When do PRM assays make sense?
Considerations for PRM method development
Live Demo

## Slide 3: Definition of PRM
PRM = MRM-HR = HR-MRM = Targeted Full Scan MS/MS
Closest spiritual cousin is triple-quad based MRM/SRM, but:
SRM
Q3 mass analyzer
m/z1
m/z2
m/z3
PRM
mass analyzer
m/z range
b1
y1
y4
b6
y5-H2O
y8
y5
P-H3PO4
Discrete transitions, hardware selected
Full scan

## Slide 4: Definition, continued
Assay is completely deterministic
Precursor m/z (list) is specified
  Possibly scheduled
  Quadrupole or ion trap selection/isolation
Fragmentation is performed
  Any kind is OK
Full MS/MS spectrum is recorded
  Any analyzer: Orbitrap, TOF, scanning quad, ion trap, etc.
Usually a full scan MS spectrum is also periodically recorded
  Two chances to verify and quantify!

## Slide 5: Common configuration: high resolution mass analyzer
Orbitrap or TOF
Precursor cycle vs. Acquisition loop cycle
  Precursor cycle: time it takes to loop through precursor list
    May vary during method
    Governs points across peak
  Acquisition loop cycle: Time from full scan to full scan with intervening # of MS/MS
    May affect instrument performance, full scan points across peak
MS1
MS21
MS22
MS2…
MS2n

## Slide 6: When do PRMs make sense?
Exquisite selectivity required
  Unit (quadrupole) vs. ppm (hi-res)
Post-translational modification localization is required
  GVDQ(pS)PLTPAGGK vs. GVDQSPL(pT)PAGGK
Rapidly convert discovery data to targeted assay
  Stay within platform
You don’t have a triple quad!
  But still want the benefits of targeted proteomics

## Slide 7: High resolution adds value to selectivity
20x
Kme3SAPATGGVKprKprPHR10
KacSAPATGGVKprKprPHR10
20x
20x
20x
ABI 5500 triple quad
ABI 5500 triple quad
QE
QE
m/z 551.9940 z=3
m/z 551.9819 z=3

## Slide 8: PTM Localization – shared ions, differential ions
Differentially Phosphorylated Peptides
With Same Base Sequence

## Slide 9: Discovery Proteomics to PRM – Short version / Label Free
Shotgun MS/MS*
Database Search
Target Selection
Spectral Library
Skyline Doc
Method/Precursor List Export
Acquire Data
Skyline Quant
* iRT peptides recommended

## Slide 10: Discovery Proteomics to PRM – Long version
Acquire Data
Skyline Quant
Shotgun w/ iRT
Database Search
Target Selection
Make Labeled Peptides
QC / Spectral Library
iRT Model
Transition, Scheduling and Gradient Optimization in Background
Skyline Doc
External Data

## Slide 11: Planning ahead for success
Strongly consider including iRT peptides in every single sample you run in your lab
  Diverse retention times, well spaced
  High enough levels to trigger MS/MS
    Or, include targeted scans
    Or, determine RTs with precursor quant in Skyline
  This can also be very beneficial for scheduling tight windows
Use a search engine supported by Skyline spectral library import
Set up your funky PTMs in advance in your document
Learn about Skyline’s secret PTM notation for import

## Slide 12: Document refinement
Keep a lot of transitions around initially
  You can always get rid of them later
  You can take them from the spectral libraries
  In theory: the more transitions, the more signal-to-noise
    Also in theory more sensitive than MRM, but generally not in practice
Take advantage of the raw data spectrum viewer functionalities
  Helpful for both MS and MS/MS inspection
Use that high res!
  Narrow your import m/z tolerances
  Inspect the ppm errors

## Slide 13: The all important dotp
dotp = dot product
  Metric of observed transition relative intensities in comparison with spectral library example
Better than a search engine score!
  Expect > 0.9 under most circumstances
Extremely useful in differentiating among similar analytes
Spectral library quality important
  Garbage in, garbage out

## Slide 14: Standardization Considerations
Label free
  Requires high degree of system reproducibility
  Hard to compare samples longitudinally
Synthetic peptides
  Highest degree of rigor
  Highest cost in time, $
  More optimization required
SILAC
  Increases complexity, chance for interference
  Standard is “prenormalized”
  Consider growing up a vat of standard for longitudinal performance
Chemical labels? (+ standards?)

## Slide 15: Data analysis considerations
Be patient, use all metrics at your disposal
Consider time window import limits
  But relies on RT or other indicators in spectral library / RT models
Consider further minimizing your document when happy with data
  Hi-res data, skyd files get big

## Slide 16: “Research Grade” PRM Concept
A quantitative, targeted proteomics assay suitable for “everyday” use
Ideally standardized with synthetic peptides (or SILAC)
Rapid design cycle using discovery data/platform
Enables longitudinal comparisons across days, months, years
Output useful for rapidly guiding biology
NOT:
  Obsessed with LOD/LOQ
  Suitable for clinical deployment

## Slide 17: Histones and their post-translational modifications
Source: PDB 1AOI, Luger et al. Nature (1997)
NH2-A R T K Q T A R K
S T G G K A P R K Q…
ph
ac
me
me
me
me
Associated with transcriptional regulatory states of genomic loci

## Slide 18: Sample preparation process and standardization
Agilent Bravo LH – fully automated
96-well SPE – semi-automated
Day 1
Day 2
Day 3