## Slide 1: Agenda
Welcome from the Skyline team!
Jump start DIA analysis with DDA data in Skyline
Introduction with Brendan MacLean
  Workflow overview
  Method overview and considerations
  Alternative workflows
Live tutorial with Jarrett Egertson – Contributor – DIA
Audience Q&A – submit questions to Google Form:
http://tinyurl.com/QA4Skyline (also in chat window)

## Slide 2: Chromatography-based Quantification
Hypothesis testing (Verification)
SRM
MS1 chromatogram extraction
Targeted MS/MS (PRM)
Data independent acquisition (DIA/SWATH)
Acquisition | Targeted | Survey
More Selective | PRM | DIA
Less Selective | SRM | MS1
Got HYPOTHESIS??

## Slide 3: Multiple Instrument Vendors

## Slide 4: Webinar 1 Overview
DDA Acquisition
Spectrum Matching
Chromatogram Extraction
Spectral Library
Building
iRT Library
Building
Product Ion
Targeting
Quantitative
Analysis

## Slide 5: Overview
DDA Acquisition
DIA Acquisition

## Slide 6: Prior Knowledge and Consistency
Relative product ion abundance
  Spectral libraries
Retention time
  iRT libraries
Powerful enough to be used cross-lab / cross experiment
  Measure, store, re-use
More powerful run-to-run
Notes: Confidence in what is being measured

## Slide 7: Relative Product Ion Abundance

## Slide 8: Retention Time
DDA run
0.5

## Slide 9: Retention Time
DDA run
0.5

## Slide 10: Retention Time
DDA run
0.5

## Slide 11: Retention Time
4
DDA run
DDA run
DDA run
DDA run
DDA run

## Slide 12: Data Independent Acquisition (DIA)
20 20 m/z-wide windows = 400 m/z
m/z
400
800
Notes: Switch to 20, put in some MS1 scans
Usually 1,000 – 5,000 peptides identified by MS/MS
Usually ~25,000 – 50,000 MS features detected
2-20% of Features Annotated
BUT Usually only ~70% overlap in annotated features between runs

## Slide 13: Data Independent Acquisition (DIA)
Scan 1
20 20 m/z-wide windows = 400 m/z
m/z
400
800
Notes: Switch to 20, put in some MS1 scans
Usually 1,000 – 5,000 peptides identified by MS/MS
Usually ~25,000 – 50,000 MS features detected
2-20% of Features Annotated
BUT Usually only ~70% overlap in annotated features between runs

## Slide 14: Data Independent Acquisition (DIA)
Scan 1
20 20 m/z-wide windows = 400 m/z
m/z
400
400
Scan 2
Notes: Switch to 20, put in some MS1 scans
Usually 1,000 – 5,000 peptides identified by MS/MS
Usually ~25,000 – 50,000 MS features detected
2-20% of Features Annotated
BUT Usually only ~70% overlap in annotated features between runs

## Slide 15: Data Independent Acquisition (DIA)
Scan 1
20 20 m/z-wide windows = 400 m/z
m/z
400
800
Scan 2
Scan 3
Scan 4
Scan 5
Scan 6
Scan 7
Scan 20
…
Scan 21
Notes: Switch to 20, put in some MS1 scans
Usually 1,000 – 5,000 peptides identified by MS/MS
Usually ~25,000 – 50,000 MS features detected
2-20% of Features Annotated
BUT Usually only ~70% overlap in annotated features between runs

## Slide 16: Data Independent Acquisition (DIA)
20 20 m/z-wide windows = 400 m/z
m/z
400
800
Time
~2 seconds
~30 seconds
Venable, J.D. et al. Nat. Meth. 2004. Gillet, L.C. et al. MCP 2012
Notes: Add in MS1 scans here

## Slide 17: Extraction of Fragment Ions
m/z
500
900
400
600
800
1000
1200
1400
51.2
51.3
51.4
51.5
51.6
51.7
0
1
2
3
4
Intensity x 10-5
m/z
Retention Time

## Slide 18: Extraction of Fragment Ions

## Slide 19: Measuring Precursor Ions
20 20 m/z-wide windows = 400 m/z
m/z
400
800
Time
~2 seconds
MS Scan
Notes: Add in MS1 scans here

## Slide 20: Precursor and Product Ion Information

## Slide 21: DIA Chromatogram Extraction
Ion Source
CID
Q1 / Trap
Mass
Analyzer
MS/MS scans
time (scan #)
intensity
m/z
m/z
m/z
m/z
20 m/z isolation

## Slide 22: Product Ion Selectivity
2 m/z
ANFQGAITNR
Notes: Show the spectrum, and the chromatogram
Even with DDA >30% of the spectra are mixed
Quantitation can be limited by interference, show 10 m/z vs. 20 m/z (from overlap experiment)
Spectrum and chromatogram from loq data on a yeast background peptide

## Slide 23: Product Ion Selectivity (DIA)
20 m/z
ANFQGAITNR
Notes: Show the spectrum, and the chromatogram
Even with DDA >30% of the spectra are mixed
Quantitation can be limited by interference, show 10 m/z vs. 20 m/z (from overlap experiment)
Spectrum and chromatogram from loq data on a yeast background peptide

## Slide 24: When Selectivity Becomes Sensitivity
Decreasing noise increases signal-to-noise

## Slide 25: DIA Trade-Offs
Selectivity
Cycle time
Measured range
All ion digital record – image quality?

## Slide 26: Overview
DDA Acquisition
Spectrum Matching
Chromatogram Extraction
Spectral Library
Building
Product Ion
Targeting
Quantitative
Analysis
DIA Acquisition
Got HYPOTHESIS??

## Slide 27: DIA-Centric Workflow
Peptide Detection
Chromatogram Extraction
Spectral Library
Building
Product Ion
Targeting
Quantitative
Analysis
DIA Acquisition
Got HYPOTHESIS??

## Slide 28: DIA-Centric Workflow
DIA Acquisition
  Pecan - MacCoss
  MS Pathfinder - Smith
  Umpire - Nesvizhskii
  Bandeira
Peptide Detection

## Slide 29: Prior Knowledge Workflow
Chromatogram Extraction
Spectral Library
iRT Library
Product Ion
Targeting
Quantitative
Analysis
DIA Acquisition
Relative Ion Abundance
Normalized RT

## Slide 30: Prior Knowledge Workflow
Chromatogram Extraction
Chromatogram Library
Product Ion
Targeting
Quantitative
Analysis
DIA Acquisition
Relative Ion Abundance
Normalized RT

## Slide 31: Prior Knowledge Workflow
Chromatogram Extraction
Product Ion
Targeting
Quantitative
Analysis
DIA Acquisition
Spectronaut
PeakView
Assay Library
Relative Ion Abundance
Normalized RT

## Slide 32: Tutorial
DIA using interspersed DDA

## Slide 33: Learn More
Webinar #3: Tuesday, Jan. 13th – PRM
Weeklong Targeted Proteomics Course at UW
  March 23-27 (apply by Nov. 21)
Workshops at US HUPO and ASMS
Weeklong Course at ETH, Zurich
  June 22-26
Weeklong Course at PRBB, Barcelona
  November 15-20
Weeklong Course in Boston
  TBA

## Slide 34: Questions?
Ask any questions you have on the topic of using DDA data in Skyline. http://tinyurl.com/QA4Skyline
Take the post-webinar survey: http://tinyurl.com/Survey4Webinar